## Slide 1: Advanced system on Chip (Soc)
Presented by: Shivani P Dusane and Shivaum S Heranjal
Department of Electrical and Computer Engineering
Submitted to:- Dr. Lauren Christopher

## Slide 2: Project Concept
Edge Detection :
Edge detection allows users to observe the features of an image for a significant change in the gray level.
Edges indicate the end of one region in the image and the beginning of another.
Application of edge detection in numerous fields in the real world:
Digital forensics, where information can be extracted from tampered videos or images
Medical imaging, study of anatomical structure, X-Rays, CT-Scans, etc.
Robotics, Autonomous vehicles, quality inspection.
Satellite image analysis.

## Slide 3: Project Concept
Sobel Filters
When using Sobel Edge Detection, the image is processed in the X and Y directions separately first, and then combined to form a new image which represents the sum of the X and Y edges of the image.
This was our 3x3 coefficient matrix, however, various other dimensional approximations exist (5x5, 7x7).

## Slide 4: System Flow Diagram
1. Webcam integration
2. Sobel Filter implementation in HW & SW
3. Monitor Display integration

## Slide 5
Frames fetched by webcam
Hardware Processing
Initially the webcam is accepting images in real time.
Dual core ARM Cortex A9 is processing the data.
Software Processing
The output fetched from previous section is used to calculate Gradient.
Monitor Display using HDMI
Each processed image is displayed using base overlay through HDMI on a monitor at every step in loop.
Number of frames can be user defined
In this section using the Hardware of Xilinx board the Sobel x, y filtering is processed on the images parallelly.
Processing System
Other hardwares used are DMAs which is used to send and receive data between PS and PL
Comparing SW and HW outputs.
Filtering is done using the SW as well (scipy), also final outputs are displayed using matplot lib in notebook.

## Slide 6: Block Diagram

## Slide 7: Flowchart

## Slide 8: Project Implementation Hardware
Coefficients for Sobel Y (vertical filter)
SOBEL X,
SOBEL Y
We are using the Dual core Arm cortex A9 processor.
Using the AXI lite buses and DMAs data is being sent and received to and from the processing system, memory.
Coefficients for Sobel Y (vertical filter)
IP Hierarchy (Sobel Y)

## Slide 9: Project Implementation Software
Gradient calculation
Webcam frames acquisition

## Slide 10: Project Implementation Software
Reshaping of 2D imgs to 1D
Sending and receiving data from the buffers using DMA
Sending out data to the HDMI

## Slide 11: Project Summary

## Slide 12: Time Comparison
Hardware execution of Sobel x and Sobel y, is over 200 times faster than that of the SW execution.
However, the total time doesn’t retain the speedup factor since the gradient calculation in software acts as a bottleneck.

## Slide 13
Input Images

## Slide 14
Hardware Output

## Slide 15: Software Output

## Slide 16: Monitor Output
Sobel x
Sobel y
Gradient

## Slide 17: Conclusion
We were able to accomplish all the proposed objectives stated at the start of the project in the proposal.
We got familiar with the Vivado software across all the lab projects and homework throughout the semester.
We leveraged this familiarity to first simplify the block design from Lab 5 by using one DMA for both read/write operations and later adding a Sobel y filter IP to process input data parallelly and send it back to the memory using the DMA.

## Slide 18: Future Scope
Integration of base overlay with custom overlay.
Removing the gradient calculation bottleneck.
This work can be expanded to implement any 3x3 separable filters for image processing.
HDMI in port could be leveraged to get real time video from the webcam and apply image processing to all incoming frames and then display on the monitor

## Slide 19: Challenges
Sobel Y filter implementation
The Sobel x filter IP design had decomposed the 3x3 kernel into 1x3 horizontal and 3x1 vertical kernels and implemented them using separate 1D FIR filters, the input data went to the horizontal filter first, whose outputs went to the vertical filter and then scaled (dividing by 8) and shifted to 0-255 range (addition by 128) for final output.
For the Sobel y filter, we took a copy of the Sobel X and changed the coefficients. However, we were getting minor “glitches” where few pixels around the edge were completely black or white, we had to face this issue till the last week where we thought of changing the order of the 1D filters, we first processed the data with the vertical filter and then with the horizontal filter and it resolved our “glitch” issue

## Slide 20: Challenges
Visually comparing HW & SW outputs
While processing SD card images, we first got Black and White outputs in SW (Figure 13) while grayscale outputs in HW this made us doubt the HW implementation.
we decided to connect a custom gaussian filter IP to the Sobel outputs in the block diagram and then subtracting gaussian outputs from the Sobel outputs to obtain the final x, y outputs to further process the gradient. This blur and subtraction process acted as a sharpening which got us the Black and White outputs like SW.
However, on integration of webcam and further discussion with professor, we realized that including a gaussian filter to the design meant, we weren’t comparing Sobel SW (which was grayscale now) to Sobel HW anymore (Sobel + Gaussian HW now). Therefore, we removed the custom Gaussian IP block from our block design and reverted to pure Sobel HW implementation.
The only setback we have now is that our HW gradient is grayscale while the SW gradient is Black and White.